## Slide 1: Flex robotics: a versatile sample changer for macromolecular crystallography applications
Control software and MxCube integration

## Slide 2: Flex robotics variants
FlexED3
FlexED8
FlexHCD
ED8 : EdgeDewar8
ED3 : EdgeDewar3
HCD : High Capacity Dewar

## Slide 3: Dewars
ED8: EdgeDewar8
  Patented EMBL design
  Open (no ports)
  Self cleaning
  Permits short dewar access
  Eight uni-puck footprint slots
  ProxiSens puck detection system
HCD: High Capacity Dewar
  Modified ESRF design
  12 SC3 puck footprint & 12 uni-puck puck footprint
  ProxiSens puck detection system

## Slide 4: Control software architectures
Two ≠ software architecture with same StaubCom device server
MxCube
StaubCom
low level server
Java high level control software
Python client
StaubCom
protocol
StaubCom protocol
Exporter
protocol

## Slide 5: StaubCom generic device server and API for Staubli robots
Socket based Ethernet communication with clients
Core Features:
  Keep-alive messages
  Update and log messages about robot status
  Dynamic loading of custom movement sequences and custom PLCs
The API permits to implement custom:
  Movement sequences
  PLCs
  Variable and IO state notification to the client
  Initialization and termination scripts
  Log and error messages
software.embl-em.de

## Slide 6: Control software architecture
MxCube
StaubCom
low level server
Java high level control software
Python client
StaubCom
protocol
StaubCom protocol
Exporter
protocol

## Slide 7: Flex robotics control architecture with Java
StaubCom
Protocol
Socket
(Ethernet)
movement sequences:
Loading
Unloading
…
VAL3
Modbus
(Ethernet)
Tango, Tine, Exporter, WebServices, Epics, …
VAL3 StaubCom server
OneWire:
Gripper identification
DM reader
ProxiSense Card:
Puck presence & type detection
Camera + image processing:
Gripper calibration
Pin detection
beamline control software (e.g.: MxCube)
IO management
PLCs for low level regulation tasks

## Slide 8: Control software architecture
MxCube
StaubCom
low level server
Java high level control software
Python client
StaubCom
protocol
StaubCom protocol
Exporter
protocol

## Slide 9: Flex robots MxCube integration
Based on the GenericSampleChanger class (Alaxandre Gobbo)
Development done by Akim Khadrouche (former BM14 technician)
Communication using Exporter protocol (JLib)
Supports events
Error and log messages
Robot status

## Slide 10: Sample changers with Java control software & StaubCom device server / API
Flex robots
  FlexHCD : ID30B - ESRF
  FlexED8 : BM14 (dismanteled) - ESRF
  FlexED3 : HTXLab – EMBL
Other sample changers
  RoboDiff : Massif 1 - ESRF
  NSLS-II Sample Changer: 17.ID.1 & 17.ID.2 - BROOKHAVEN

## Slide 11: RoboDiff and ESRF-Flex-HCD
RoboDiff (Massif-1)
  SPINE Sample Changer
  Diffractometer
  VAL3 integration of external devices
ESRF-FlexHCD
  Versatile sample changer
  External devices helping the sample handling

## Slide 12: ESRF-FlexHCD Control software architecture
StaubCom device server
Python client integrated in a Bliss device server
MxCube
StaubCom
low level server
Java high level control software
Python client
StaubCom
protocol
StaubCom protocol
Exporter
protocol

## Slide 13: ESRF-FlexHCD Control software architecture
StaubCom device server
Python client integrated in PyFlex BLISS controller :
      Trajectories handling :
            Ueye camera image analysis (Lima library)
            Microscan Data matrix reading (Ethernet socket)
            Cached variable updates
      External device :
            1-wire memory reading (pyowfs)
            Proxisense card (serial line socket)
      Logging of StaubCom and PyFlex + Command line debugging option
      No GUI
      automatically exported as a generic TANGO server

## Slide 14: ESRF-FlexHCD integrated in MX-CuBE2
Sample Changer Tab using the generic sample changer Class :
  Sample position list
  Basic commands:
    Loading / unloading
    change gripper
    Sample reset
    Abort
Data collection list:
    Chained loading
    Automatic processing

## Slide 15: Acknowledgements
EMBL:
  Gergely PAPP
  Marcos LOPEZ-MARRERO
  Christopher ROSSI
  Robert JANOCHA
  Franck FELISAZ
  Clement SOREZ
  Florent Cipriani
  Andrew MC CARTHY
  Hassan BELRHALI
  Akim KHADROUCHE
  Babu MANJASETTY
  Stephen CUSACK
ESRF:
  Didier Nurizzo
  Matias Guijarro
  Antonia Beteva
  Fabien Dobias
  Hugo Caserotto
  Thierry Giraud
  Pascal Theveneau
  Gordon Leonard