## Slide 1
IMPROVING ABSTRACTIONS
(HARDWARE OBJECTS POINT OF VIEW)
Antonia BETEVA

## Slide 2: IMPROVING ABSTRACTIONS – Current status
Current status
      8 Hardware Objects – 5 procedures and 4 equipment
      GenericSampleChanger, GenericDiffractometer, Minidiff…
Problems
      Different constraints from the control systems
      Imposing methods (using the abc module) depending on who is writing the HO.
      AbstractCollect, AbstractMultiCollect.
      Needs change when adding new hardware.

## Slide 3: IMPROVING ABSTRACTIONS - proposal
Distinguish between sequences (procedures) and equipment
      Generic* – sequences only
      Abstract* - equipment only
Define only minimum variables and methods
      For procedures
        methods like start/execute/stop/pause...
        use cleanup, error_cleanup (with statement).
      For equipment
        only methods shared for all the similar equipment.
        provide a Mockup class to simulate missing equipment.
      Use abc with parsimony (or not?)
        Methods needed by the GUI.
      Use “standard” log/error report.

## Slide 4: IMPROVING ABSTRACTIONS - proposal
All specific methods in specific class(es)
      Site specific, Beamline specific, Hardware specific
…but
      Share same equipment HO between different sites
        Create equipment specific HO (MD2Motor, SardanaMotor...)
        Improve MD2Motor rather than create ESRFMD2Motor.

## Slide 5: IMPROVING ABSTRACTIONS – procedure example
AbstractEnergyScan
Methods imposed by the GUI
      With a known signature – startEnergyScan
      (element,edge,directory,prefix,session_id=None,blsample_id=None)
      With free signature – scanCommandStarted
      (*args, **kwargs )
      Legacy methods - isConnected
Two compulsory (but empty methods)
      escan_cleanup, escan_error_cleanup
      def escan_cleanup(self):
      pass
ESRF EnergyScan – inherits from Abstract
      Methods Shared by all the beamlines – doChooch
ID29 EnergyScan – inherits from ESRF
      Beamline specific methods

## Slide 6: IMPROVING ABSTRACTIONS – Equipment example
GenericMCA
Imposed methods
      start_acq (cnt_time=None)
        Keyword Args:
        cnt_time (float, optional): count time [s]; 0 means to count indefinitely
        Returns:
        None
      read_data(chmin, chmax, calib=False)
        Keyword Args:
        chmin (float): channel number or energy [keV]
        chmax (float): channel number or energy [keV]
        calib (bool): use calibration, defaults to Fals
        Returns:
        numpy.array. x - channels or energy (if calib=True), y - data.
ESRFMCA – inherits from GerericMCA
      MCA specific methods - get/set roi, get/set calibration
      Detector specific methods - get/set presets
RontecMCA – inherits forom GenericMCA