## Slide 1
MXCuBE status @ ALBA
XALOC Beamline
Roeland Boer, Beamline Responsible XALO @ ALBA
MXCuBE meeting, Feb 2018, Diamond Light Source

## Slide 2
Overview
MXCuBE2 @ ALBA
Highlights @ BL13-XALOC beamline
MXCuBE Current Status
MXCuBE Next steps

## Slide 3
Integration of MXCuBE 2 (Qt4) @ ALBA
Xaloc Beamline (BL-13)
Beamline control based on SARDANA + TAURUS + TANGO

## Slide 4
MXCuBE 2 implementation @ ALBA
Graphical User Interface
Control Layer
Hardware Repository
Bliss Framework Common
Bliss Framework
python 2.x and Qt4
Over Tango and Sardana/Taurus control layer
Sardana/Taurus
Beamline Hardware and Data
Tango DS
Hardware Objects
ALBA + MXCuBE specifics

## Slide 5
MXCuBE 2 @ ALBA
Current Status @ BL13-XALOC

## Slide 6
MXCuBE 2 @ ALBA
Working on Qt4/master branch.
Bixente Rey collaboration.
MXCuBE interface for all individual beamline elements.
Sample mounting (mxCATS) and centering commissioned and tested on users
Testing basic collection method implementation.
ISPyB testing stage (Daniel Salvat)
Two new Tango DS implemented XALOC:
  Diffractometer
  Beamline Supervisor
Current Status @ BL13-XALOC

## Slide 7
Integration of MXCuBE 2 @ ALBA
XalocDiffractometer TANGO DS
XALOC Diffractometer
Phase transitions
GoBeamViewPhase,
GoCollectPhase,
GoSampleVisuPhase,
GoTransferPhase
Parameters
Beamstoptype,
MountingPosition,
PinLenght,
SampleMode,
...
EPS signals
KappaPresence,
Ln2coverOpen,
SampleOnMagnet,
...
Goniometer
omega, omegax,
omegay, omegaz,
centx, centy,
kappa.
Detector Table
diftabx,
diftabz.
DUSP
yagy,
yagz.
Aperture
aperx,
aperz.
Beamstop
bsx,bsy,bsz,
bstopx,
bstopz.
Any HwObj from MXCuBE will always operate the equipment through this Tango DS.

## Slide 8
Integration of MXCuBE 2 @ ALBA
XalocBeamlineSupervisor TANGO DS
XALOC Beamline Supervisor
Devices
Diffractometer,
SampleChanger,
Cryostream,
Shutters
EPS signals
DetDistanceSafe,
DetCoverOpen,
CryoPosition,
FastShutterCollectPosition.
Phase transitions
GoBeamViewPhase,
GoCollectPhase,
GoSampleVisuPhase,
GoTransferPhase
Function: Coordinate devices’s operation and configuration for phase transitions

## Slide 9: Screenshots of MXCuBE 2 @ ALBA

## Slide 10: Screenshots of MXCuBE 2 @ ALBA

## Slide 11
MXCuBE 2 @ ALBA
Collection being commissioned
Data processing needs full implementation
Testing on friendly users soon
Final throes

## Slide 12
Acknowledgements
The people
BL13-XALOC
Roeland Boer
Judith Juanhuix
Fernando Gil
Barbara Machado
Xavi Carpena
IT-Systems
Sergi Puso
Ramon Escriba
Thank you for your attention
MIS
Daniel Salvat
Alfonso Burgos
Controls
Guifre Cuni
Jordi Andreu
Externals
Bixente Rey

## Slide 13
Thank you for your attention