## Slide 1: Status of NFPSS MX Beamlines at SSRF
Wenming Qin
National Facility for Protein Science in Shanghai (NFPSS)
/Shanghai Synchrotron Radiation Facility (SSRF)
November, 2023

## Slide 2: Shanghai Synchrotron Radiation Facility
SSRF Ring Parameters
Electron Energy：3.5 GeV
Electron Current: 300 mA
Circumference: 432 m
Straight sections: 20
Soft X-ray Free Electron Laser
Hard X-ray Free Electron Laser
SSRF

## Slide 3: National Facility for Protein Science . Shanghai
NFPS passed the National Acceptance Review, and formally opened to the users in July 2015.
NFPS is composed of 9 technology systems with state-of-the-art instruments in its Haike Road Campus and 5 Beamlines within the Shanghai Synchrotron Radiation Facility.

## Slide 4: MX Beamlines at SSRF
6 MX Beamlines
BL17B
BL18U1
BL19U1
BL17UM
BL02U1
BL10U1
NFPSS
Shanghai Tech
SSRF
MXCube
MOF/COF, GIWAXS, XANS

## Slide 5: MXCUBE Status
What we did
What we improved
What we are planning to do
We are still at the very beginning!

## Slide 6: What We Did
MXCube 3 installed in virtual system
Exporter with MD2 in virtual system
EPICS-Pilatus with Pilatus3S-2M/Pilatus3-6M detector
EPICS for Energy，Fluo-detector，Detector distance，Ring Current、Intensity
Frame monitor and autoload with ADXV by monitoring the temp files in /lima_data directory
Data auto processing pipeline with XDS, autoproc xia2-dials.
Control the Actor sample changer system with socket communication
MXCube3 at BL17B and BL19U have opened to users from Feberary, 2023 and June, 2023
Replaced with braggy

## Slide 7: MXCUBE3 Interface and Communication Protocols Among Hardware Components with Diffraction Results Displayed in BRAGGY

## Slide 8
Pipeline of Data Processing and Structure Analysis
for small molecular crystals
MySQL
Xia2-xds
autoPROC
Ins file
HKL file
Data collection
Xia2-dials
DATA Process
ShelXT
ShelXS
ShelxD
Structure Analysis
format conversion
.........

## Slide 9
Web page of Data Processing result

## Slide 10
Auto restart mxcube program
Some restart shortcut on the desktop in order to allow users do the reset work themselves

## Slide 11: What progress we made from last meeting in May
Operating and improving the mxcube3 at BL19U1 by fixing bugs.
Replaced the adxv image viewer with braggy system.
Replaced the MD2 with MD2-S.
Allow users to load there own sample information by an excel file into mxcube before data collection.
ISPyB installation and configuration of python version

## Slide 12
Live view of the diffraction images based on Braggy web page
Get the FilePath through EPICS
Tracing the latest image with Braggy

## Slide 13
Using tango to poll the image from video-server of MD2-S
the video is clearer and smoother
with the B-zoom than before.
Thanks to Bernard from Arinax, the B-zoom camera is Integrated with tango
(getjpeg at BL17B with exporter)

## Slide 14
Loading sample file path information in advance
By using python tkinter program

## Slide 15
More features of Mxcube are implemented
1. Customized collection
2. Auto loop centering

## Slide 16
https://github.com/ispyb/py-ispyb
https://github.com/ispyb/py-ispyb-ui
https://github.com/ispyb/ISPyB
https://github.com/ispyb/EXI
ISPyB
Java version is used to get the basic function
ISPYB version：
  1. java √
    Full-featured
    ISPYB
      Backend Server
    EXI
      GUI
    LDAP
      Authentication
  2. Python
    Functionality in development

## Slide 17: Project progress
1. Database Configure
  In debugging, it was found that some tables are required, but they are deleted in the database script.
2. LDAP Configure
3. ISPYB compiled and deployed in WildFly application Server
4. Mxcube now can login by Ispyb service.

## Slide 18: Software Architecture
ISPyB database

## Slide 19: What We are Planning to Do
FLEX-ED35
FLEX-ED35 will be installed at BL19U1 next year.
Complete the configuration of ISPyB and connect the database with MXCuBE.
Complete the function of automatic sample mounting, centering and collection.
Set up mxcube at BL18U1

## Slide 20
Thank you for your attention!
Acknowledgments:
- Shanghai Sychrontron Radiation Facility
- Mikel Eguiraun and Jie Nan from MAX IV
- Letícia G. Capovilla from LNLS
- Arinax, Dectris, Rigaku, Irelec
- MXCube community.